## Slide 1
SETU
Structural Evaluation and Thickness Underwriting
A Reliability-Based Framework for Residual-Life Prediction and Maintenance Prioritisation of Concrete Pavements
Research proposal — supervisory review
[Name] · Department of Civil Engineering · [Institution]
Supervisor: [Supervisor]

## Slide 2
The problem
Designed once from assumptions; never checked until it cracks
A rigid pavement slab is designed once, in an office, using single representative values — and is never revisited against the conditions actually realised on site.
Design parameter | Assumed | Reality | CoV
Subgrade reaction, k | one value | varies continuously along alignment | 0.20 – 0.35
Flexural strength, MR | one value | varies pour to pour, season to season | 0.10 – 0.15
Elastic modulus, E | one value | varies with mix and maturity | 0.10 – 0.15
Slab thickness, h | nominal | construction tolerance | 0.02 – 0.05
Traffic | projection | projection error and overloading | 0.15 – 0.30
The industry's answer is a blanket safety factor applied everywhere — so concrete is wasted where conditions are good, and slabs fail early where they are not. Both happen on the same project.
SETU — Structural Evaluation and Thickness Underwriting
1

## Slide 3
“Which 200 metres of this 40 km road
will fail first — and what will it cost me?”
No design office, asset owner or software product can answer this today.
The data needed already exists — pour registers, cube results, subgrade tests, traffic counts. It has simply never been joined to the damage model that produced the design.
SETU — Structural Evaluation and Thickness Underwriting
2

## Slide 4
The approach
Four layers — the code is the foundation, not the casualty
LAYER 1 — Mechanistic core
Westergaard stresses · Bradbury warping · IRC:58 fatigue · Miner summation
→ Deterministic damage, every value clause-traceable
LAYER 2 — Probabilistic propagation
Monte Carlo over distributions of k, MR, E, h and traffic
→ P(failure) and reliability per segment
LAYER 3 — ML residual correction
Gaussian Process on (predicted − observed) distress
→ Corrected forecast with calibrated confidence
LAYER 4 — Decision engine
Cost of acting now vs probability-weighted cost of waiting
→ Ranked maintenance plan, with money attached
At zero variability the framework reduces EXACTLY to the deterministic IRC:58 result — verified by automated test. It extends the code; it does not replace it.
SETU — Structural Evaluation and Thickness Underwriting
3

## Slide 5
Why the ML is constrained
Three independent reasons, any one of which is sufficient
Professional accountability
No engineer will stake a seal on a number whose provenance is “the neural network said so”. A codal computation plus a bounded correction remains open to professional scrutiny.
Data efficiency
The physics carries the signal; the model fits only a small residual. Useful accuracy is attainable with a few hundred observations rather than tens of thousands.
Regulatory admissibility
Output that cites the governing clause is admissible in project documentation. Output that cannot be traced is not.
SETU — Structural Evaluation and Thickness Underwriting
4

## Slide 6
Result — reliability-based thickness
Same corridor, same traffic, same concrete. Only the subgrade differs.
Subgrade | k (MPa/mm) | h for 90% reliability | vs. uniform design
Very good | 0.200 | 285 mm | 15 mm saved
Good | 0.150 | 295 mm | 5 mm saved
Fair | 0.110 | 300 mm | reference
Poor | 0.080 | 305 mm | 5 mm more required
Very poor | 0.045 | 320 mm | 20 mm more required
A 35 mm spread across one corridor.
Uniform design conceals this entirely: it over-builds the good ground and under-builds the bad. One computation corrects both.
Computed with the implemented engine. Indicative coefficients of variation; project-specific values to be substituted.
SETU — Structural Evaluation and Thickness Underwriting
5

## Slide 7
Result — thermal warping frequently governs
300 mm slab · 15 t axle · ΔT 16.8 °C day / 8.4 °C night
Analysis | Stress (MPa) | Stress ratio | Assessment
Load only | 2.055 | 0.457 | below endurance limit — appears safe
Load + warping (BUC governs) | 3.625 | 0.806 | well above endurance limit
Omitting thermal warping understates the stress ratio by 43 per cent.
Because the fatigue relationship is steeply non-linear in the stress ratio, this becomes an order-of-magnitude error in allowable repetitions. Warping is not a refinement — it frequently governs.
Bradbury coefficient evaluated from a continuous fitted function (max deviation 0.023 from the published curve, 1 ≤ L/l ≤ 14) rather than a tabulated lookup — original work, and differentiable for later optimisation.
SETU — Structural Evaluation and Thickness Underwriting
6

## Slide 8
What is already built
This is not a concept — the core is running and tested
Component | Contents | Status
Analytical stress module | Westergaard interior / edge / corner, radius of relative stiffness, equivalent radius | 9 tests passing
Thermal warping module | Bradbury coefficient (fitted), edge and interior warping, BUC and TDC checks | 21 tests passing
Damage module | Stress ratio, 3-branch fatigue law, Miner summation, residual life, erosion index | 22 tests passing
Reliability module | Monte Carlo propagation, P(failure), reliability-based thickness search | included above
Public web calculator | Browser-based, offline-capable, full calculation trace, no data collected | 4 parity tests
56 automated tests, all passing. The browser calculator agrees with the Python reference to 3.4 × 10⁻¹⁵ — verified by test, not by inspection.
SETU — Structural Evaluation and Thickness Underwriting
7

## Slide 9
What I am asking for
Guidance, and access — not funding
1
Approval of the direction
Confirmation that the reliability-based extension of IRC:58 is a sound and defensible line of research for the thesis.
2
One corridor of data
Introduction to a concessionaire, PWD circle or consultant willing to share construction and condition records for a single stretch. This is the critical dependency for Objective 6.
3
Publication guidance
Advice on the appropriate venue — an IRC/ICI journal or an international transportation journal — and on what must be strengthened before submission.
4
A view on scope
Whether to prioritise depth on the mechanistic and reliability layers, or to proceed to the machine-learning layer once field data is in hand.
SETU — Structural Evaluation and Thickness Underwriting
8

## Slide 10
Work plan
24 months, two phases
Months | Activity | Milestone
1 – 3 | Literature consolidation; variability statistics for Indian materials and subgrades | Parameter database
3 – 6 | Extend mechanistic core: temperature differential regimes, erosion criterion | Extended Layer 1
5 – 9 | Probabilistic layer refinement and verification | Validated Layer 2
7 – 12 | Corridor identification; acquisition of construction and condition records | Field dataset
12 – 16 | Retrospective validation against documented distress | Accuracy established
14 – 19 | Machine-learning residual layer | Validated Layer 3
18 – 21 | Decision engine and maintenance prioritisation | Layer 4 complete
20 – 24 | Demonstration study, documentation, dissemination | Publications; final report
SETU — Structural Evaluation and Thickness Underwriting
9

## Slide 11
The mechanics already exist in IRC:58.
What is missing is its probabilistic extension,
its application forward in time,
and its calibration against the records
that construction already generates.
No instrumentation. No proprietary software. No significant capital.
A verified computational core is already implemented.